## Slide 1: PROGRAMMABLE LOGIC CONTROLLER (PLC) LOGIC SCHEMATICS

## Slide 2: AGENDA
INTRODUCTION:
  Welcome
  Introduction and Course Overview
  Activities Overview
  Ice Breaker
  PLC Logic Schematics Pre Assessment
SESSION I:
Identify Schematic Symbols
  N. O. and N. C. vs. Examine On and Examine Off
SESSION II:
Converting Relay Logic to Ladder Logic
Activities: LogixPro Introductory Lab
  Break

## Slide 3: AGENDA
SESSION III:
Branch Instructions and Internal Bits
Activities: LogixPro Door Simulation Lab
LUNCH
SESSION III:
Activities: LogixPro Door Simulation Lab (Cont’d)

## Slide 4: AGENDA
SESSION IV:
Boolean Logic
Break
Activities: LogixPro Silo Lab
REVIEW AND REFLECTION
FINAL ASSESSMENT

## Slide 5: GENERAL AND ELECTRICAL SAFETY COURSE OVERVIEW
COURSE OVERVIEW:
16 hours over two days includes lecture and activities
Provides knowledge and skills necessary to identify, read, and program PLC Logic schematics

## Slide 6: INTRODUCTON TO PLC LOGIC SCHEMATICS COURSE OUTCOMES
At the conclusion of this course, participants should be able to identify, read, and program PLC Logic schematics related to:
Identify Schematic Symbols
  N. O. and N. C. vs. Examine On and Examine Off
Converting Relay Logic to Ladder Logic
Branch Instructions and Internal Bits
Boolean Logic
PLC Timers
PLC Counters

## Slide 7: SESSION I
IDENTIFY SCHEMATIC SYMBOLS

## Slide 8: SESSION I: LEARNING OBJECTIVES
At the conclusion of this session, participants will understand principles related to:
Identify Schematic Symbols
  Normally Open
  Normally Closed
  Examine On
  Examine Off

## Slide 9
Normally Open & Normally Closed
VS.
Examine On & Examine Off

## Slide 10
NORMALLY OPEN
Without any external force or pressure a normally open contact remains open
When external force or pressure is applied a normally open contact closes

## Slide 11
NORMALLY CLOSED
Without any external force or pressure a normally closed contact remains closed
When external force or pressure is applied a normally closed contact opens

## Slide 12
EXAMINE ON
Examine on is true when it is on
Examine on is false when it is off

## Slide 13
EXAMINE OFF
Examine off is true when it is off
Examine off is false when it is on

## Slide 14
NORMALLY OPEN & NORMALLY CLOSED
EXAMINE ON & EXAMINE OFF
Associated with the flow of electricity
Associated with the flow of logic

## Slide 15
NORMALLY OPEN & NORMALLY CLOSED
L1
L2
CR-1
CR1-1
CR1-2
R
G

## Slide 16
NORMALLY OPEN & NORMALLY CLOSED
L1
L2
CR-1
CR1-1
CR1-2
R
G

## Slide 17: WHAT WILL HAPPEN IN THE FOLLOWING CIRCUIT WHEN THE SWITCH IS OPEN?
When the switch is open, the N.C. contact remains closed and the green light is energized, while the N.O. contact remains open and the red light remains off

## Slide 18
L1
L2
CR-1
CR1-1
CR1-2
R
G
OPEN SWITCH

## Slide 19
L1
L2
CR-1
CR1-1
CR1-2
R
G
NORMALLY OPEN & NORMALLY CLOSED

## Slide 20: WHAT WILL HAPPEN IN THE FOLLOWING CIRCUIT WHEN THE SWITCH IS CLOSED?
When the switch is closed, the N.C. contact opens and the green light is off, while the N.O. contact closes and the red light is energized

## Slide 21
CLOSED SWITCH
L1
L2
CR-1
CR1-1
CR1-2
R
G

## Slide 22
Inputs
Outputs
Ladder Logic Program
O/0
O/1
I/0
EXAMINE ON & EXAMINE OFF
I/0
I/0
O/0
O/1
L1
L2

## Slide 23
Inputs
Outputs
Ladder Logic Program
O/0
O/1
I/0
Which output if any will energize in this circuit?
I/0
I/0
O/0
O/1
L1
L2

## Slide 24
Inputs
Outputs
Ladder Logic Program
O/0
O/1
I/0
EXAMINE ON & EXAMINE OFF
I/0
I/0
/2
O/0
O/1
L1
L2
FALSE
OFF
TRUE
ON

## Slide 25
Inputs
Outputs
Ladder Logic Program
O/0
O/1
I/0
Which output if any will energize in this circuit?
I/0
I/0
O/0
O/1
L1
L2

## Slide 26
Inputs
Outputs
Ladder Logic Program
O/0
O/1
I/0
EXAMINE ON & EXAMINE OFF
I/0
I/0
O/0
O/1
L1
L2
FALSE
OFF
TRUE
ON

## Slide 27
Inputs
Outputs
Ladder Logic Program
O/0
O/1
I/0
I/1
I/2
Look at the inputs and determine which output will energize
I/0
I/0
I/1
I/1
I/2
I/2
O/0
O/1
L1
L2
I/0
I/1
I/2
O/2
O/2

## Slide 28
Inputs
Outputs
Ladder Logic Program
O/0
O/1
I/0
I/1
I/2
All inputs are open/off, so output O/1 is energized
I/0
I/0
I/1
I/1
I/2
I/2
O/0
O/1
L1
L2
I/0
I/1
I/2
O/2
O/2

## Slide 29
Inputs
Outputs
Ladder Logic Program
O/0
O/1
I/0
I/1
I/2
Look at the inputs and determine which output will energize
I/0
I/0
I/1
I/1
I/2
I/2
O/0
O/1
L1
L2
I/0
I/1
I/2
O/2
O/2

## Slide 30
Inputs
Outputs
Ladder Logic Program
O/0
O/1
I/0
I/1
I/2
Output O/2 will energize
I/0
I/0
I/1
I/1
I/2
I/2
O/0
O/1
L1
L2
I/0
I/1
I/2
O/2
O/2

## Slide 31
Inputs
Outputs
Ladder Logic Program
O/0
O/1
I/0
I/1
I/2
Look at the inputs and determine which output will energize
I/0
I/0
I/1
I/1
I/2
I/2
O/0
O/1
L1
L2
I/0
I/1
I/2
O/2
O/2

## Slide 32
Inputs
Outputs
Ladder Logic Program
O/0
O/1
I/0
I/1
I/2
I/0
I/0
I/1
I/1
I/2
I/2
O/0
O/1
L1
L2
I/0
I/1
I/2
O/2
O/2
Output O/0 will energize

## Slide 33
Inputs
Outputs
Ladder Logic Program
O/0
O/1
I/0
I/1
I/2
Look at the inputs and determine which output will energize
I/0
I/0
I/1
I/1
I/2
I/2
O/0
O/1
L1
L2
I/0
I/1
I/2
O/2
O/2

## Slide 34
Inputs
Outputs
Ladder Logic Program
O/0
O/1
I/0
I/1
I/2
I/0
I/0
I/1
I/1
I/2
I/2
O/0
O/1
L1
L2
I/0
I/1
I/2
O/2
O/2
Output O/1 will energize

## Slide 35
Inputs
Outputs
Ladder Logic Program
O/0
O/1
I/0
I/1
I/2
Look at the inputs and determine which output will energize
I/0
I/0
I/1
I/1
I/2
I/2
O/0
O/1
L1
L2
I/0
I/1
I/2
O/2
O/2

## Slide 36
Inputs
Outputs
Ladder Logic Program
O/0
O/1
I/0
I/1
I/2
I/0
I/0
I/1
I/1
I/2
I/2
O/0
O/1
L1
L2
I/0
I/1
I/2
O/2
O/2
Output O/2 will energize

## Slide 37
Inputs
Outputs
Ladder Logic Program
O/0
O/1
I/0
I/1
I/2
Look at the inputs and determine which output will energize
I/0
I/0
I/1
I/1
I/2
I/2
O/0
O/1
L1
L2
I/0
I/1
I/2
O/2
O/2

## Slide 38
Inputs
Outputs
Ladder Logic Program
O/0
O/1
I/0
I/1
I/2
I/0
I/0
I/1
I/1
I/2
I/2
O/0
O/1
L1
L2
I/0
I/1
I/2
O/2
O/2
Output O/1 will energize

## Slide 39
DETERMINING THE FLOW OF LOGIC WITH BRANCH INSTRUCTIONS
  Branch instructions are used to create parallel path for logic instructions to flow
  When determining the flow of logic begin at the top of the ladder diagram and trace a logic path from left to right
  When an instruction is false the flow of logic stops and moves downward in the program

## Slide 40
DETERMINING THE FLOW OF LOGIC WITH BRANCH INSTRUCTIONS
When an instruction is false move down in the program and look for another path
When a path of true instructions exists from left to right, then the output is energized

## Slide 41
Inputs
Outputs
Ladder Logic Program
O/0
I/0
I/1
I/2
I/0
I/0
I/1
I/1
I/2
O/0
L1
L2
I/2
I/0
Look at the inputs and determine if output O/0 will energize

## Slide 42
Inputs
Outputs
Ladder Logic Program
O/0
I/0
I/1
I/2
I/0
I/0
I/1
I/1
I/2
O/0
L1
L2
I/2
I/0
Look for a path that allows for the flow of logic

## Slide 43
Inputs
Outputs
Ladder Logic Program
O/0
I/0
I/1
I/2
I/0
I/0
I/1
I/1
I/2
O/0
L1
L2
I/2
I/0
Look for a path that allows for the flow of logic

## Slide 44
Inputs
Outputs
Ladder Logic Program
O/0
I/0
I/1
I/2
I/0
I/0
I/1
I/1
I/2
O/0
L1
L2
I/2
I/0
Look for a path that allows for the flow of logic

## Slide 45
Inputs
Outputs
Ladder Logic Program
O/0
I/0
I/1
I/2
I/0
I/0
I/1
I/1
I/2
O/0
L1
L2
I/2
I/0
Look for a path that allows for the flow of logic

## Slide 46
Inputs
Outputs
Ladder Logic Program
O/0
I/0
I/1
I/2
I/0
I/0
I/1
I/1
I/2
O/0
L1
L2
I/2
I/0
Yes

## Slide 47
Inputs
Outputs
Ladder Logic Program
O/0
I/0
I/1
I/2
I/0
I/0
I/1
I/1
I/2
O/0
L1
L2
I/1
I/0
Look at the inputs and determine if output O/0 will energize

## Slide 48
Inputs
Outputs
Ladder Logic Program
O/0
I/0
I/1
I/2
I/0
I/0
I/1
I/1
I/2
O/0
L1
L2
I/1
I/0
Look for a path that allows for the flow of logic

## Slide 49
Inputs
Outputs
Ladder Logic Program
O/0
I/0
I/1
I/2
I/0
I/0
I/1
I/1
I/2
O/0
L1
L2
I/1
I/0
Look for a path that allows for the flow of logic

## Slide 50
Inputs
Outputs
Ladder Logic Program
O/0
I/0
I/1
I/2
I/0
I/0
I/1
I/1
I/2
O/0
L1
L2
I/1
I/0
Look for a path that allows for the flow of logic

## Slide 51
Inputs
Outputs
Ladder Logic Program
O/0
I/0
I/1
I/2
I/0
I/0
I/1
I/1
I/2
O/0
L1
L2
I/1
I/0
Look for a path that allows for the flow of logic

## Slide 52
Inputs
Outputs
Ladder Logic Program
O/0
I/0
I/1
I/2
I/0
I/0
I/1
I/1
I/2
O/0
L1
L2
I/1
I/0
Look for a path that allows for the flow of logic

## Slide 53
Inputs
Outputs
Ladder Logic Program
O/0
I/0
I/1
I/2
I/0
I/0
I/1
I/1
I/2
O/0
L1
L2
I/1
I/0
No I/2 must be open/off for O/0 to energize

## Slide 54
Inputs
Outputs
Ladder Logic Program
O/0
I/0
I/1
I/2
I/0
I/0
I/1
I/1
I/2
O/0
L1
L2
I/1
I/0
Now with I/2 being open/off, output O/0 will energize

## Slide 55
M
L1
L2
STOP 1
STOP 2
START 1
START 2
M1
OL
Two Station Start/Stop Motor Control

## Slide 56
M
L1
L2
STOP 1
STOP 2
START 1
START 2
M1
OL
Two Station Start/Stop Motor Control
Stops are in Series
Starts are in Parallel

## Slide 57
M
L1
L2
STOP 1
STOP 2
START 1
START 2
M1
OL
N.O. & N.C Representation of a two Station Start/Stop Motor Control
Stops are in Series
Starts are in Parallel

## Slide 58
M
L1
L2
STOP 1
STOP 2
START 1
START 2
M1
Ladder Logic Representation of a two Station Start/Stop Motor Control
Stops are in Series
Starts are in Parallel

## Slide 59: CONVERTING RELAY LOGIC TO LADDER LOGIC
SESSION II

## Slide 60: SESSION II: LEARNING OBJECTIVES
At the conclusion of this session, participants will understand principles related to:
  Relay Logic Instructions
  Converting Hardwired Circuits

## Slide 61: RELAY LOGIC INSTRUCTIONS
L
U

## Slide 62: EXAMINE ON OR EXAMINE IF CLOSED (XIC)
Examine On refers to a normally open contact instruction in a logic ladder program
Examine On is true if its addressed bit is on (1)
Examine On is false if its addressed bit is off (0)

## Slide 63: EXAMINE OFF OR EXAMINE IF OPEN (XIO)
Examine off refers to a normally closed contact instruction in a logic ladder program
Examine off is true if its addressed bit is off (0)
Examine off is false if its addressed bit is on (1)

## Slide 64
OUTPUT INSTRUCTIONS
L
U
An Output instruction bit becomes true (1) when a complete path of logic exists
A Latching Output instruction bit that emulates the latching action of a latching relay
An Unlatching Output instruction bit de-energizes a latching output that has the same address

## Slide 65
NEW RUNG AND BRANCH INSTRUCTIONS
The new rung instruction adds a rung to the ladder logic diagram
The branch instruction adds a parallel logic path within a rung

## Slide 66
ADDRESSING BIT INSTRUCTIONS
Instruction addressing formats vary from one PLC family to another
The address identifies the function of an instruction and links it to a particular bit in the data portion of the memory
Address are formatted as file type, slot number, and bit number

## Slide 67
ADDRESSING BIT INSTRUCTIONS
I:1/1
File Type
Slot Number
Bit Number
File Types
Input - I:1/2
Output - O:1/0
Internal Bit- B3:2/3
Timer – T4:0
Counter – C5:0

## Slide 68
CONVERTING HARDWIRED CIRCUITS
S 1
PL
S 1
PL

## Slide 69
CONVERTING HARDWIRED CIRCUITS
S 1
PL
L 1
S 1
PL
L 1

## Slide 70
CONVERTING HARDWIRED CIRCUITS
PB 1
PL
PB 2
PB 1
PL
PB 2
Convert to PLC Ladder Logic

## Slide 71
CONVERTING HARDWIRED CIRCUITS
PB 1
PL
PB 2
PL
Convert to PLC Ladder Logic

## Slide 72
CONVERTING HARDWIRED CIRCUITS
PB 1
PL
PB 2
PL

## Slide 73
CONVERTING HARDWIRED CIRCUITS
LS 1
PL
LS 2
LS 3
Convert to PLC Ladder Logic
LS 4

## Slide 74
CONVERTING HARDWIRED CIRCUITS
LS 1
PL
LS 2
LS 3
LS 4

## Slide 75
CONVERTING HARDWIRED CIRCUITS
CR
PL
PB 1
CR
What will happen if PB 1 is pushed?

## Slide 76
CONVERTING HARDWIRED CIRCUITS
CR
PL
PB 1
CR

## Slide 77
CONVERTING HARDWIRED CIRCUITS
CR
PL
PB 1
CR
Convert to PLC Ladder Logic

## Slide 78
PB 1
PL
CONVERTING HARDWIRED CIRCUITS

## Slide 79
CONVERTING HARDWIRED CIRCUITS
STOP
FWD
REV
F
R
R-1
F-1
F-2
R-2
What will happen if FWD is pushed?

## Slide 80
CONVERTING HARDWIRED CIRCUITS
STOP
FWD
REV
F
R
R-1
F-1
F-2
R-2
What will happen if FWD is released?

## Slide 81
CONVERTING HARDWIRED CIRCUITS
STOP
FWD
REV
F
R
R-1
F-1
F-2
R-2
What will happen if REV is pushed?

## Slide 82
CONVERTING HARDWIRED CIRCUITS
STOP
FWD
REV
F
R
R-1
F-1
F-2
R-2
Nothing

## Slide 83
CONVERTING HARDWIRED CIRCUITS
STOP
FWD
REV
F
R
R-1
F-1
F-2
R-2
What will happen if Stop is pushed?

## Slide 84
CONVERTING HARDWIRED CIRCUITS
STOP
FWD
REV
F
R
R-1
F-1
F-2
R-2

## Slide 85
CONVERTING HARDWIRED CIRCUITS
STOP
FWD
REV
F
R
R-1
F-1
F-2
R-2
What will happen if REV is pushed?

## Slide 86
CONVERTING HARDWIRED CIRCUITS
STOP
FWD
REV
F
R
R-1
F-1
F-2
R-2
What will happen if REV is released?

## Slide 87
CONVERTING HARDWIRED CIRCUITS
STOP
FWD
REV
F
R
R-1
F-1
F-2
R-2
What will happen if FWD is pushed?

## Slide 88
CONVERTING HARDWIRED CIRCUITS
STOP
FWD
REV
F
R
R-1
F-1
F-2
R-2
Nothing

## Slide 89
CONVERTING HARDWIRED CIRCUITS
STOP
FWD
REV
F
R
R-1
F-1
F-2
R-2
What will happen if Stop is pushed?

## Slide 90
CONVERTING HARDWIRED CIRCUITS
STOP
FWD
REV
F
R
R-1
F-1
F-2
R-2

## Slide 91
CONVERTING HARDWIRED CIRCUITS
Convert to PLC Ladder Logic
STOP
FWD
REV
F
R
R-1
F-1
F-2
R-2

## Slide 92
CONVERTING HARDWIRED CIRCUITS
Address the Bit Instructions
STOP
FWD
REV
F
R
R-1
F-1
F-2
R-2

## Slide 93
CONVERTING HARDWIRED CIRCUITS
I:0/0
I:0/1
I:0/2
F
R
O:0/1
O:0/0
O:0/0
O:0/1
O:0/1
O:0/0
What will happen if 1:0/1 is pushed?

## Slide 94
CONVERTING HARDWIRED CIRCUITS
I;0/0
I:0/1
I:0/2
F
R
O:0/1
O:0/0
O:0/0
O:0/1
O:0/1
O:0/0
What will happen if 1:0/1 is released?

## Slide 95
CONVERTING HARDWIRED CIRCUITS
I;0/0
I:0/1
I:0/2
F
R
O:0/1
O:0/0
O:0/0
O:0/1
O:0/1
O:0/0
1:0/1 goes false, but O:0/0 remains on

## Slide 96
CONVERTING HARDWIRED CIRCUITS
I;0/0
I:0/1
I:0/2
F
R
O:0/1
O:0/0
O:0/0
O:0/1
O:0/1
O:0/0
What will happen if 1:0/2 is pushed?

## Slide 97
CONVERTING HARDWIRED CIRCUITS
I;0/0
I:0/1
I:0/2
F
R
O:0/1
O:0/0
O:0/0
O:0/1
O:0/1
O:0/0
1:0/2 is true but O:0/1 remains off

## Slide 98
CONVERTING HARDWIRED CIRCUITS
STOP 1
START 1
M-1
M-2
M-1
M-2
START 2
STOP 2
Convert to PLC Ladder Logic

## Slide 99
CONVERTING HARDWIRED CIRCUITS
STOP 1
START 1
M-1
M-2
M-1
M-2
START 2
STOP 2
M-1
Address the Bit Instructions

## Slide 100
CONVERTING HARDWIRED CIRCUITS
I:0/0
I:0/1
M-1
M-2
O:0/0
O:0/1
I:0/3
I:0/2
O:0/0
O:0/0
O:0/1
What will happen if I:0/1 is pushed?

## Slide 101
CONVERTING HARDWIRED CIRCUITS
I:0/0
I:0/1
M-1
M-2
O:0/0
O:0/1
I:0/3
I:0/2
O:0/0
O:0/0
O:0/1
O:/0/0 is true but O:0/1 remains false

## Slide 102
CONVERTING HARDWIRED CIRCUITS
I:0/0
I:0/1
M-1
M-2
O:0/0
O:0/1
I:0/3
I:0/2
O:0/0
O:0/0
O:0/1
What will happen if I:0/1 is released?

## Slide 103
CONVERTING HARDWIRED CIRCUITS
I:0/0
I:0/1
M-1
M-2
O:0/0
O:0/1
I:0/3
I:0/2
O:0/0
O:0/0
O:0/1
I:0/1 goes false but O:0/0 remains on

## Slide 104
CONVERTING HARDWIRED CIRCUITS
I:0/0
I:0/1
M-1
M-2
O:0/0
O:0/1
I:0/3
I:0/2
O:0/0
O:0/0
O:0/1
What will happen if I:0/3 is pushed ?

## Slide 105
CONVERTING HARDWIRED CIRCUITS
I:0/0
I:0/1
M-1
M-2
O:0/0
O:0/1
I:0/3
I:0/2
O:0/0
O:0/0
O:0/1
Output O:0/1 becomes true

## Slide 106
CONVERTING HARDWIRED CIRCUITS
I:0/0
i:0/1
M-1
M-2
O:0/0
O:0/1
i:0/3
i:0/2
O:0/0
O:0/0
O:0/1
What will happen if I:0/3 is released?

## Slide 107
CONVERTING HARDWIRED CIRCUITS
I:0/0
I:0/1
M-1
M-2
O:0/0
O:0/1
I:0/3
I:0/2
O:0/0
O:0/0
O:0/1
I:0/3 goes false but o:0/1 remains true

## Slide 108
CONVERTING HARDWIRED CIRCUITS
I:0/0
I:0/1
M-1
M-2
O:0/0
O:0/1
I:0/3
I:0/2
O:0/0
O:0/0
O:0/1
What will happen if I:0/0 is pushed?

## Slide 109
CONVERTING HARDWIRED CIRCUITS
I:0/0
I:0/1
M-1
M-2
O:0/0
O:0/1
I:0/3
I:0/2
O:0/0
O:0/0
O:0/1
I:0/0 goes false causing both rungs to go false

## Slide 110: ACTIVITY: LOGIXPRO INTRODUCTORY LAB
EXERCISE:
RSLogix Program Creation

## Slide 111
  Enjoy your break!
BREAK
TIME

## Slide 112
BRANCH INSTRUCTIONS & INTERNAL BITS
SESSION III

## Slide 113: SESSION III: LEARNING OBJECTIVES
At the conclusion of this session, participants will understand principles related to:
  Branch instructions
  Branch types
  Programing limitations of PLC
  Internal Relay instructions (Internal Bit)

## Slide 114
TYPICAL BRANCH INSTRUCTION
A
B
C

## Slide 115
Branch instructions are used to create parallel paths of input conditions. This allows for more than one path of logic to establish continuity in a rung
Input branching by formation of parallel branches can be used in a program to allow a combination of input conditions
If at least one branch forms a true logic path, the rung logic is true and the output will energize
BRANCH INSTRUCTIONS

## Slide 116
PARALLEL INPUT BRANCHES
A
C
D
B

## Slide 117
A
C
D
B

## Slide 118
A
C
D
B

## Slide 119
PARALLEL OUTPUT BRANCHES
A
B
C
D

## Slide 120
A
B
C
D

## Slide 121
BRANCHING WITH CONDITIONS
Additional input logic instructions can be programmed in the output branches to enhance conditional control of the outputs
When a true path of logic exists to the output branch, including extra conditions allows for greater control of the outputs
For example: Two sump pumps, a main and auxiliary pump are responsible for drainage. If the main pump can’t keep up with demand the auxiliary pump would start up

## Slide 122
PARALLEL OUTPUT BRANCHES WITH CONDITIONS
A
B
D
E
C

## Slide 123
PARALLEL OUTPUT BRANCHES WITH CONDITIONS
A
B
D
E
C

## Slide 124
A
B
D
E
C

## Slide 125
NESTED BRANCHES
Nesting, is a branch within a branch. Input and output branches can be nested to avoid redundant instructions and to speed up processor scan time. A nested branch starts or ends within another branch
In some PLC models, the programming of a branch circuit within a branch, or nesting, can not be done directly. It is possible though to program an equivalent branching condition

## Slide 126
NESTED OUTPUTS
A
B
E
F
C
D
G
A Branch within
a Branch

## Slide 127
NESTED INPUT
A
E
Y
B
D
A Branch within
a Branch
C

## Slide 128
REMOVING NESTED INPUT
A
E
Y
B
D
Instruction C repeated
C
C

## Slide 129
PROGRAMMING LIMITATIONS OF PLCS
  Vertical Contacts (Not Allowed)
  Number of Series Contacts on 1 Rung (Typically)
  Number of Parallel Branches on 1 Rung (Typically)

## Slide 130
PROGRAMMING LIMITATIONS OF PLCS
  Number of Series Contacts on 1 Rung (Typically)
  Number of Outputs on 1 Rung (Typically)

## Slide 131
VERTICAL CONTACTS
Because PLCs scan the logic of a program from left to right and top to bottom only, programming of vertical contacts is not allowed. Vertical contacts can be removed from programming by determining all the paths of logic that flows thru the vertical contact and rewriting it horizontally

## Slide 132
A
B
D
E
C
Y
PROGRAM WITH A VERTICAL CONTACT

## Slide 133
A
B
D
E
C
Y
REWRITE PROGRAM TO ELIMINATE VERTICAL CONTACT

## Slide 134
A
B
D
E
C
Y
FIRST DETERMINE ALL PATHS FOR LOGIC TO FLOW

## Slide 135
A
B
D
E
C
Y
FIRST DETERMINE ALL PATHS FOR LOGIC TO FLOW
A-D

## Slide 136
A
B
D
E
C
Y
FIRST DETERMINE ALL PATHS FOR LOGIC TO FLOW
A-D
B-E

## Slide 137
A
B
D
E
C
Y
FIRST DETERMINE ALL PATHS FOR LOGIC TO FLOW
A-D
B-E
B-C-D

## Slide 138
A
B
D
E
C
Y
FIRST DETERMINE ALL PATHS FOR LOGIC TO FLOW
A-D
B-E
B-C-D
A-C-E

## Slide 139
A
B
D
E
Y
REWRITE THE PROGRAM ELIMINATING THE VERTICAL CONTACT INSTRUCTION
B
C
D
E
A
C

## Slide 140
Maximum of 10 Input Instructions
MAX.
7
Lines

## Slide 141
1 2 3 4 5 6 7 8 9 10 11 12 13
The number of Instructions Exceeds the Horizontal Limit
O/0
USING THE INTERNAL BIT TO SOLVE HORIZONTAL PROGRAMMING LIMITATIONS

## Slide 142
1 2 3 4 5 6 7
The number of Instructions can be split into two rungs using an Internal Bit
B3:1/0
USING THE INTERNAL BIT TO SOLVE HORIZONTAL PROGRAMMING LIMITATIONS
8 9 10 11 12 13
O/0
B3:1/0
Internal Bit

## Slide 143: ACTIVITY: LOGIXPRO DOOR SIMULATION LAB
EXERCISE:
Door Simulation Lab – Exercises 1 and 2

## Slide 144
  Enjoy your lunch!
LUNCH
TIME
Notes: Key Message | N/A
Background Knowledge | N/A
Interactivity | Questions/comments
Notes | Instructor specifies the exact time the participants are expected to return to class

## Slide 145: ACTIVITY: LOGIXPRO DOOR SIMULATION LAB
EXERCISE:
Door Simulation Lab – Exercises 1 and 2 (Cont’d)

## Slide 146
BOOLEAN LOGIC
SESSION IV

## Slide 147: SESSION IV: LEARNING OBJECTIVES
At the conclusion of this session, participants will understand principles related to:
  And, Or, and Not functions
  Variations of And, Or, and Not functions

## Slide 148
AND, OR, & NOT FUNCTIONS
AND, OR, and NOT, are the three fundamental logic functions performed by digital equipment
Each function has it’s own symbol, and a rule that determines the outcome of the logic
Variations of these functions include the NAND gate, (AND NOT) and the NOR gate, (OR NOT)

## Slide 149
THE AND FUNCTION
The AND function, also known as an AND gate is a device where two inputs in series and must be examined on in order for the output to energize

## Slide 150
AND TRUTH TABLE |  | 
INPUTS |  | OUTPUT
A | B | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 151
VARIATIONS OF AND
BOOLEAN SYMBOL
LADDER LOGIC
A
B
Y
BOOLEAN ALGEBRA (A X B) = Y

## Slide 152
THE OR FUNCTION
The OR function, also known as an OR gate is a device where two inputs are in parallel. Any one of the inputs can be true in order for the output to energize

## Slide 153
OR TRUTH TABLE |  | 
INPUTS |  | OUTPUT
A | B | Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 154
Variations of OR
BOOLEAN SYMBOL
LADDER LOGIC
A
B
Y
BOOLEAN ALGEBRA (A + B) = Y

## Slide 155
THE NOT FUNCTION
Input A
NOT A
The NOT function is mainly used in conjunction with the AND or the OR gate in order to invert the input from a 1 status to a 0 status

## Slide 156
NOT TRUTH TABLE | 
A | NOT A
0 | 1
1 | 0

## Slide 157
VARIATIONS OF THE NOT FUNCTION
Input A
NOT A
BOOLEAN SYMBOL
LADDER LOGIC
BOOLEAN ALGEBRA A = Y
A
Y

## Slide 158
THE NAND GATE
The NAND function, also known as the NAND gate is a device where one of two inputs in series must examine off in order for the output to energize

## Slide 159
NAND TRUTH TABLE |  | 
INPUTS |  | OUTPUT
A | B | Y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 160
VARIATIONS OF NAND
BOOLEAN SYMBOL
LADDER LOGIC
A
B
Y
BOOLEAN ALGEBRA (A X B) = Y
(A X B) = Y
(A X B) = Y

## Slide 161
Exclusive OR
The exclusive OR (XOR) function, is a device where only one of two inputs in parallel can examine on in order for the output to energize. It is commonly used for the comparison of two binary numbers

## Slide 162
(XOR) TRUTH TABLE |  | 
INPUTS |  | OUTPUT
A | B | Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 163
Exclusive NOR
The exclusive NOR (XNOR) function, is a device where two inputs in parallel must either examine on, or examine off, in order for the output to energize

## Slide 164
EXCLUSIVE NOR TRUTH TABLE |  | 
INPUTS |  | OUTPUT
A | B | Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 165
Inputs |  | Truth Table Outputs for each Gate |  |  |  |  | 
A | B | AND | NAND | OR | NOR | EX-OR | EX-NOR
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1 | 0 | 0 | 1

## Slide 166
  Enjoy your break!
BREAK
TIME
Notes: Key Message | N/A
Background Knowledge | N/A
Interactivity | Questions/comments
Notes | Instructor specifies the exact time the participants are expected to return to class

## Slide 167: ACTIVITY: LOGIXPRO SILO LAB
EXERCISE:
The Silo Lab Utilizing Relay Logic – Exercises 1 and 2
Notes: Key Message | N/A
Background Knowledge | N/A
Interactivity | Questions/comments
Notes | This slide is self-explanatory; the Instructor will not need to provide additional information

## Slide 168: AGENDA
RECAP
SESSION IV:
Activity: LogixPro Silo Lab (Cont’d)
SESSION V:
PLC Timers
Activity: LogixPro Introduction to Timers Lab
  Break
  Activity: LogixPro Introduction to Timers Lab (Cont’d)
  LUNCH

## Slide 169: AGENDA
SESSION VI:
PLC Counters
Activity: LogixPro Introduction to Counters Lab
Break
Activity: LogixPro Batch Mixing Lab
REVIEW AND REFLECTION
PLC LOGIC SCHEMATICS FINAL ASSESSMENT

## Slide 170: ACTIVITY: LOGIXPRO SILO LAB
EXERCISE:
The Silo Lab Utilizing Relay Logic – Exercises 1 and 2 (Cont’d)
Notes: Key Message | N/A
Background Knowledge | N/A
Interactivity | Questions/comments
Notes | This slide is self-explanatory; the Instructor will not need to provide additional information

## Slide 171: INTRODUCTION TO PLC TIMERS
SESSION V

## Slide 172: SESSION V: LEARNING OBJECTIVES
At the conclusion of this session, participants will understand principles related to:
  Timer instructions
  Timer quantities
  Calculating timer duration
  Timer bits
  Timer types

## Slide 173
TIMER INSTRUCTIONS
PLC timers are the most commonly used PLC instruction, after coils and contacts
PLC timer instructions provide the same functions as on-delay and off-delay timers
PLC timers offer several advantages over real world mechanical and electronic timers

## Slide 174
TIMER ADVANTAGES
Time setting can be easily set or changed
Timers can be added or removed from circuit through the use of programming rather than wiring changes
Timer accuracy and repeatability are extremely high

## Slide 175
TIMER QUANTITIES
Preset Time: This represents the time duration for the timing circuits
Accumulated Time: This represents the amount of time that has elapsed from the moment the timing circuit began
Time Base: The time base is a preset interval that the timer count. Typical time bases are: 1, 0.1 and 0.01

## Slide 176
TON
Timer On Delay
Timer T4:1
Time Base 0.1
Preset 100
Accumulated 0
EN
DN
I:1/0
To calculate the duration of a timer multiply the preset value by the time base
The above timers duration is set for 10 seconds
100 x 0.1 = 10
CALCULATING TIMER DURATION

## Slide 177
CALCULATING TIMER DURATION
What is the duration of the following timer?
The above timers duration is set for 1 second
100 x 0.01 = 1
TON
Timer On Delay
Timer T4:1
Time Base 0.1
Preset 100
Accumulated 0
EN
DN
I:1/0

## Slide 178
CALCULATING TIMER DURATION
What is the duration of the following timer?
The above timers duration is set for 30 seconds
300 x 0.1 = 30 seconds
TON
Timer On Delay
Timer T4:1
Time Base 0.1
Preset 100
Accumulated 0
EN
DN
I:1/0

## Slide 179
TIMER BITS
Enable Bit: The Enable Bit, (EN) is true when ever the timer instruction is true
Timer -Timing Bit: The Timer-Timing Bit, (TT) is true whenever the accumulated value of the timer is changing, meaning the timer is timing
Done Bit: The Done Bit, (DN) changes state whenever the accumulated value equals the preset value. Its state depends on the type of timer being used

## Slide 180
TIMER TYPES
IN GENERAL, THERE ARE THREE TYPES OF PLC TIMERS
On-delay Timer: (TON)
Off-delay Timer: (TOF)
Retentive Timer: (RTO)

## Slide 181
ON-DELAY TIMER INSTRUCTIONS
The On-Delay timer counts time-based intervals when the rung instruction is true
When the rung instruction containing the timer become true, the timer time out period begins

## Slide 182
ON-DELAY TIMER INSTRUCTIONS
When timer time out period ends,(Preset Value equals the Accumulated Value), an output is made true
If the rung goes false before the time out period ends, the accumulated value will reset

## Slide 183: ON DELAY TIMERS
TON
Timer On Delay
Timer T4:1
Time Base 0.1
Preset 100
Accumulated 0
EN
DN
I:1/0
O:2/0
O:2/2
O:2/1
T4:1/EN
T4:1/TT
T4:1/DN
Timer Enable Bit
Timer Timing Bit
Timer Done Bit

## Slide 184: ON DELAY TIMERS
TON
Timer On Delay
Timer T4:1
Time Base 0.1
Preset 100
Accumulated 5
EN
DN
I:1/0
O:2/0
O:2/2
O:2/1
T4:1/EN
T4:1/TT
T4:1/DN
Timer Enable Bit
Timer Timing Bit
Timer Done Bit
WHEN THE TIMER RUNG IS TRUE:
The Enable bit is true
The Timer Timing bit is also true
The Done bit is false
The timer begins timing

## Slide 185: ON DELAY TIMERS
TON
Timer On Delay
Timer T4:1
Time Base 0.1
Preset 100
Accumulated 100
EN
DN
I:1/0
O:2/0
O:2/2
O:2/1
T4:1/EN
T4:1/TT
T4:1/DN
Timer Enable Bit
Timer Timing Bit
Timer Done Bit
The Enable bit remains true
When the accumulated value equals the preset value
.

## Slide 186: ON DELAY TIMERS
TON
Timer On Delay
Timer T4:1
Time Base 0.1
Preset 100
Accumulated 100
EN
DN
I:1/0
O:2/0
O:2/2
O:2/1
T4:1/EN
T4:1/TT
T4:1/DN
Timer Enable Bit
Timer Timing Bit
Timer Done Bit
The Enable bit remains true
When the accumulated value equals the preset value
.
The Timer Timing bit goes false
The Done bit is true

## Slide 187
OFF-DELAY TIMER INSTRUCTIONS
The Off-Delay timer will keep an output energized for a set period of time after the rung containing the timer has gone false
When the rung instruction containing the timer becomes true, the Done Bit (DN) of the timer becomes true

## Slide 188
OFF-DELAY TIMER INSTRUCTIONS
When timer time out period ends,(Preset Value equals the Accumulated Value), the Done Bit goes false
If the rung goes true before the time out period ends, the accumulated value will reset to 0

## Slide 189: OFF DELAY TIMERS
TOF
Timer Off Delay
Timer T4:1
Time Base 0.1
Preset 100
Accumulated 0
EN
DN
I:1/0
O:2/0
O:2/2
O:2/1
T4:1/EN
T4:1/TT
T4:1/DN
Timer Enable Bit
Timer Timing Bit
Timer Done Bit
WHEN THE TIMER RUNG IS TRUE:
The Done Bit becomes true
The Enable bit is also true
The Timer Timing bit is false

## Slide 190: OFF DELAY TIMERS
TOF
Timer Off Delay
Timer T4:1
Time Base 0.1
Preset 100
Accumulated 10
EN
DN
I:1/0
O:2/0
O:2/2
O:2/1
T4:1/EN
T4:1/TT
T4:1/DN
Timer Enable Bit
Timer Timing Bit
Timer Done Bit
WHEN THE TIMER RUNG TRANSITIONS FROM TRUE TO FALSE:
The Done Bit remains true
The timer begins timing.

## Slide 191: OFF DELAY TIMERS
TOF
Timer Off Delay
Timer T4:1
Time Base 0.1
Preset 100
Accumulated 10
EN
DN
I:1/0
O:2/0
O:2/2
O:2/1
T4:1/EN
T4:1/TT
T4:1/DN
Timer Enable Bit
Timer Timing Bit
Timer Done Bit
WHEN THE TIMER RUNG TRANSITIONS FROM TRUE TO FALSE:
The Done Bit remains true
The timer begins timing.
The Enable bit becomes false
The Timer Timing bit becomes true

## Slide 192: OFF DELAY TIMERS
TOF
Timer Off Delay
Timer T4:1
Time Base 0.1
Preset 100
Accumulated 100
EN
DN
I:1/0
O:2/0
O:2/2
O:2/1
T4:1/EN
T4:1/TT
T4:1/DN
Timer Enable Bit
Timer Timing Bit
Timer Done Bit
When the accumulated value equals the preset value.

## Slide 193: OFF DELAY TIMERS
TOF
Timer Off Delay
Timer T4:1
Time Base 0.1
Preset 100
Accumulated 100
EN
DN
I:1/0
O:2/0
O:2/2
O:2/1
T4:1/EN
T4:1/TT
T4:1/DN
Timer Enable Bit
Timer Timing Bit
Timer Done Bit
When the accumulated value equals the preset value.
All bits go false

## Slide 194
RETENTIVE TIMER INSTRUCTIONS
The bits of a Retentive timer, act much the same as the bits for an On-Delay timer
However when the rung instruction containing the timer transitions from true to false, the accumulative value is not reset

## Slide 195
RETENTIVE TIMER INSTRUCTIONS
Loss of power to the timer after it reaches its preset value does not effect the state of the bits
A Retentive timer must be intentionally reset

## Slide 196: RETENTIVE TIMERS
RTO
Retentive Timer On
Timer T4:1
Time Base 0.1
Preset 100
Accumulated 0
EN
DN
I:1/0
O:2/0
O:2/1
T4:1/DN
T4:1/EN
Timer Done Bit
Timer Enable Bit
T4:1
I:1/1
Reset
RES
Retentive timers require a reset instruction.

## Slide 197: CASCADING TIMERS
The programming of two or more timers together is called Cascading
Timers can be interconnected to solve a variety of logic control functions

## Slide 198: CASCADING TIMERS
Cascading timers can allow you to exceed the maximum preset time of a single timer
The following slide shows how two motors can be started in sequence with a 10 second time delay using Cascading timers

## Slide 199: SEQUENCE STARTING
TON
Timer On Delay
Timer T4:1
Time Base 0.1
Preset 100
Accumulated 0
EN
DN
I:1/0
O:2/0
O:2/1
T4:1/EN
T4:2/DN
TON
Timer On Delay
Timer T4:2
Time Base 0.1
Preset 100
Accumulated 0
EN
DN
T4:1/DN
M1
M2

## Slide 200: EXTENDING TIME DELAY
TON
Timer On Delay
Timer T4:1
Time Base 0.1
Preset 30000
Accumulated 0
EN
DN
I:1/0
O:2/1
T4:2/DN
TON
Timer On Delay
Timer T4:2
Time Base 0.1
Preset 12000
Accumulated 0
EN
DN
T4:1/DN
M2

## Slide 201: ACTIVITY: LOGIXPRO INTRODUCTION TO TIMERS LAB
EXERCISE:
Introduction to RSLogix Timers
Notes: Key Message | N/A
Background Knowledge | N/A
Interactivity | Questions/comments
Notes | This slide is self-explanatory; the Instructor will not need to provide additional information

## Slide 202
  Enjoy your break!
BREAK
TIME
Notes: Key Message | N/A
Background Knowledge | N/A
Interactivity | Questions/comments
Notes | Instructor specifies the exact time the participants are expected to return to class

## Slide 203: ACTIVITY: LOGIXPRO INTRODUCTION TO TIMERS LAB
EXERCISE:
Introduction to RSLogix Timers (Cont’d)
Traffic control utilizing TON timers – Exercises 1 and 2
Notes: Key Message | N/A
Background Knowledge | N/A
Interactivity | Questions/comments
Notes | This slide is self-explanatory; the Instructor will not need to provide additional information

## Slide 204
  Enjoy your lunch!
LUNCH
TIME
Notes: Key Message | N/A
Background Knowledge | N/A
Interactivity | Questions/comments
Notes | Instructor specifies the exact time the participants are expected to return to class

## Slide 205: INTRODUCTION TO PLC COUNTERS
SESSION VI

## Slide 206: SESSION VI: LEARNING OBJECTIVES
At the conclusion of this session, participants will understand principles related to:
  Counter instructions
  Counter quantities
  Counter bits
  Counter types

## Slide 207
COUNTER INSTRUCTIONS
PLC counters can serve the same function as real world counters
All PLC manufactures offer some from of counter instructions
PLC counters are similar to timers except they do not operate on an internal clock but are dependent on external inputs for counting

## Slide 208
COUNTER TYPES
There are two types of counters, Up-Counters and Down Counters
The Up-Counter increments up by 1 every time the counter rung transitions from false to true

## Slide 209
COUNTER TYPES
The Down-Counter decrements down by 1 every time the counter rung transitions from false to true
Both the Up-Counter and Down Counter are retentive so they require a reset instruction

## Slide 210
COUNTER QUANTITIES
Preset Value: Specifies the number the counter must reach before it changes the state of the done bit. It can range from -32,768 to +32,767
Accumulated Value: Represents the current count of the counter. It can either increment up (CTU) or decrement down (CTD). It has the same range as the preset value

## Slide 211
COUNTER BITS
Count-Up (CU) Enable Bit: The count-up enable bit is true whenever the count-up counter instruction is true. If the rung instruction is false the enable bit is false

## Slide 212
COUNTER BITS
Count-Down (CD) enable Bit: The count-down enable bit is true whenever the Count-Down counter instruction is true. If the rung instruction is false the enable bit is false
Done (DN) Bit: The done bit is true when the accumulated value is equal or greater then the preset value

## Slide 213
Overflow (OV) Bit: The overflow bit is true whenever the counter counts past its maximum value of 32,767. When the limit is reached the count wraps around to -32,767 and begins to count up from there
COUNTER BITS

## Slide 214
Underflow (UN) Bit: The overflow bit is true whenever the counter counts past its minimum value of -32,767. When the limit is reached the count wraps around to +32,767 and begins to count down from there
COUNTER BITS

## Slide 215: UP-COUNTER
CTU
Count-Up Counter
Counter C5:1
Preset 100
Accumulated 0
CU
DN
I:1/0
O:2/0
O:2/1
C5:1/DN
C5:1/DN
Counter done bit
Counter done bit
C5:1
I:1/1
Reset
RES

## Slide 216: DOWN-COUNTER
CTD
Count-Down Counter
Counter C5:1
Preset 100
Accumulated 0
CU
DN
I:1/0
O:2/0
O:2/1
C5:1/DN
C5:1/DN
Counter done bit
Counter done bit
C5:1
I:1/1
Reset
RES

## Slide 217: CASCADING COUNTERS
The programming of two or more counters together is called Cascading
Cascading counters can allow you to exceed the maximum preset count of a single counter
The following slide shows how two counter can be used to exceed the maximum value of 32,767

## Slide 218: CASCADING COUNTERS
CTU
Count-Up Counter
Counter C5:1
Preset 32,000
Accumulated 0
CU
DN
I:1/0
CTU
Counter C5:2
Preset 32,000
Accumulated 0
CU
DN
C5:1/DN
Count-Up Counter
Light
C5:1/DN
C5:2/DN
I:1/0

## Slide 219: ACTIVITY: LOGIXPRO INTRODUCTION TO COUNTERS LAB
EXERCISE:
Introduction to RSLogix Counters
Notes: Key Message | N/A
Background Knowledge | N/A
Interactivity | Questions/comments
Notes | This slide is self-explanatory; the Instructor will not need to provide additional information

## Slide 220
  Enjoy your break!
BREAK
TIME
Notes: Key Message | N/A
Background Knowledge | N/A
Interactivity | Questions/comments
Notes | Instructor specifies the exact time the participants are expected to return to class

## Slide 221: ACTIVITY: LOGIXPRO BATCH MIXING LAB
EXERCISE:
Batch mix exercises utilizing PLC Counters
Notes: Key Message | N/A
Background Knowledge | N/A
Interactivity | Questions/comments
Notes | This slide is self-explanatory; the Instructor will not need to provide additional information

## Slide 222: QUESTIONS AND COMMENTS

## Slide 223: FINAL: CONCLUDING THE COURSE
  Concluding the course
  Final Assessment
  Instructor and Course Evaluation

## Slide 224
FINAL ASSESSMENT
Notes: Key Message | N/A
Background Information | N/A
Interactivity | Questions/comments
Notes | N/A